| EnzyLightTM ADP Assay Kit (EADP-100) |  |
| --- | --- |
|  |  |  | Rapid bioluminescent determination of ADP |  |  |  |

DESCRIPTION

BioAssay Systems’ EnzyI_ightTM ADP Assay Kit provides a rapid method to measure ADP levels. The assay involves two steps. In the first step, the working reagent lyses cells to release ATP and ADP. In the presence of luciferase, ATP immediately reacts with the Substrate D-luciferin to produce light. The light intensity is a direct measure of intracellular ATP concentration.

Luciferase

ATP + D-luciferin + O2	oxyluciferin + AMP + PPi + CO2 + light

In the second step, the ADP is converted to ATP through an enzyme reaction. This newly formed ATP then reacts with the D-luciferin as in the first step. Due to a special formulation of the reagent system which greatly stabilizes the light signal generated by the luciferase reaction, the luminescence from the initial ATP measurement remains stable throughout this assay. Therefore, the second light intensity measured represents the total ADP and ATP concentration in the sample.

This non-radioactive, homogeneous cell-based assay is performed in microplates. The reagent is compatible with all culture media and with all liquid handling systems for high-throughput screening applications in 96- well and 384-well plates.

KEY FEATURES

Safe. Non-radioactive assay.

Sensitive and accurate. As low as 0.1 µM ADP can be quantified. Homogeneous and convenient. "Mix-incubate-measure" type assay. No wash and reagent transfer steps are involved.

Robust and amenable to HTS: Z’ factors of 0.5 and above are routinely observed in 96-well and 384-well plates. Can be readily automated on HTS liquid handling systems for processing thousands of samples per day.

APPLICATIONS

ADP determination in cells and other biological samples.

KIT CONTENTS

Assay Buffer: 10 mL	Substrate: 120 µL

Cosubstrate: 120 µL	ATP Enzyme: 120 µL

ADP Enzyme: 120 µL	Standard: 100 µL 3 mM ADP

Storage conditions: store all reagents at -20°C. This product is shipped on dry ice. Shelf life of at least 6 months.

Precautions: reagents are for research use only. Normal precautions for laboratory reagents should be exercised while using the reagents. Please refer to Material Safety Data Sheet for detailed information.

ASSAY PROCEDURE

1. 1. Standard Curve. Prepare 1000 µI_ 30 µM ADP Premix by mixing 10 µI_ 3 mM Standard and 990 µI_ distilled water (for cell culture samples dilute ADP in culture media). Dilute standard as follows. Transfer 100 µI_ standards into wells of a white opaque 96-well plate.

| No | Premix + H2O/media | Vol (µI_) | ADP (µM) |
| --- | --- | --- | --- |
| 1 | 150 µI_ + 0 µI_ | 150 | 30 |
| 2 | 120 µI_ + 30 µI_ | 150 | 24 |
| 3 | 90 µI_ + 60 µI_ | 150 | 18 |
| 4 | 60 µI_ + 90 µI_ | 150 | 12 |
| 5 | 45 µI_ + 105 µI_ | 150 | 9 |
| 6 | 30 µI_ + 120 µI_ | 150 | 6 |
| 7 | 15 µI_ + 135 µI_ | 150 | 3 |
| 8 | 0 µI_ + 150 µI_ | 150 | 0 |

Samples. Add 100 µI_ sample per well in separate wells.

For cell cultures, plate cells (100 µI_/96well plate, 25 µI_/384well plate) in white opaque tissue culture plates. If desired, add 5 µI_ test compounds and controls dissolved in PBS or culture medium per well. Rock plate lightly to mix and incubate for desired period of time (e.g. overnight).

For other biological samples, transfer 100 µI_ (25 µI_ for 384 well plates) of the sample to wells in a white opaque titer plate.

2.	ATP Assay. Bring Assay Buffer, Substrate and Cosubstrate to room temperature. Thaw enzyme on ice or at 4°C. Fresh Reconstitution is recommended. Store unused reagents including the enzyme at -20°C.

ATP Reagent. For each 96-well, mix 95 µI_ Assay Buffer with 1 µI_ Substrate, 1 µI_ Cosubstrate and 1 µI_ ATP Enzyme. For each 384- well, mix 30 µI_ Assay Buffer with 0.6 µI_ Substrate and 0.3 µI_ ATP Enzyme.

Add ATP Reagent to each well (90 µI_/96well, 25 µI_/384well) and mix by tapping the plate. Incubate for 10 minutes at room temperature.

Read luminescence (RLU A) on a luminometer. For most luminometers
(Berthold Luminometer, LJL Analyst, Top Count, MicroBeta Counters,
CLIPR and I_eadSeeker), integration time of 0.1 to 5 sec is appropriate.

3.	ADP Assay. Prepare ADP Reagent: for each 96-well, mix 12 µI_ dH2O with 1 µI_ ADP Enzyme. For each 384-well, mix 3 µI_ dH2O with 0.25 µI_ ADP Enzyme.

Add ADP Reagent to each well (10 µI_/96well, 2.5 µI_/384well) and mix by tapping the plate or pipetting up and down. Incubate for 10 minutes at room temperature.

Read luminescence (RLU B) on a luminometer.

4.	Calculation of ADP Concentration. Subtract RLU A from RLU B for standards and samples. Plot the ARI_U versus ADP concentration for the standards. From the slope of this plot, the Sample ADP concentration can be computed with the following equation:

[ADP]sample (µM) =	Slope

[ADP]sample (µM) =	Slope

(RLU B)sample – (RI_U A)sample

0	10	20	30

0	10	20	30

[ADP] (µM)

[ADP] (µM)

300000

300000

200000

200000

100000

100000

0

0

ADP

ADP

ADP Standard Curve in Water

LITERATURE

[1].	Bradbury DA, et al (2000). Measurement of the ADP:ATP ratio in human leukaemic cell lines can be used as an indicator of cell viability, necrosis and apoptosis. J Immunol Methods. 240:79-92.

[2].	Chen-Scarabelli C, et al (2004). Turning necrosis into apoptosis: the exacting task that can enhance survival. Am Heart J. 148(2):196-9.

[3].	Crouch S, et al (1993). The use of ATP Bioluminescence as a measure of cell proliferation and cytotoxicity. J Immunol Methods, 160(1): 81-8.