Favor Thermal Shaker

with Cooling & Heating Function

Favor Thermal-Shaker for microtubes combines both shaking and cooling/heating function to serve as an ideal instrument for intensive mixing of samples under the controlled temperature conditions.

This instrument shows the following features: High Control precision, stable running, and easy to operate.  The mixing and heating modes can be operated either simultaneously or independently.  The main body of the mixing block can be chosen from a set of different types of blocks.  This product is applicable for DNA analysis, extraction of lipids and other cell components, DNA library construction, PCR reaction, pre-denaturation in electrophoresis.

Features

- Microprocessor controller with digital display is easy to setup and use

- Digital performance at analog prices

- Thermostat temperature from room temperature-10 ~ 100 ℃

- Standard and customized types of blocks are available.

- Microprocessor controls incubation time, shaking speed and temperature.

- Over high temperature alarm and Over low temperature alarm ensure safety & reliability

- Low noise working even under the speed of 1,5000rmp

- 4 types of standard blocks are interchangeable with Thermo Block Models

- Easy user calibration

- Confirmed by CE safety Standard.

Experiment Information of Block from Favorgen

Experiment Information of Block from Favorgen

| Type of Block | Parameter | Setting Temperature | Tube Temperature (I), time waste (I) | Tube Temperature (II), time waste (II) |
| --- | --- | --- | --- | --- |
| FATSM-B | 54X0.5ml | 50℃ | 49.6℃, 90 seconds | 49.8℃, 120 seconds |
| FATSM-C | 35X1.5ml | 50℃ | 49.3℃, 120 seconds | 49.6℃, 150 seconds |

Specifications

| Controller | Microprocessor Controller |
| --- | --- |
| Display | 20 x 2 LCD |
| Operating Temp. Range | -10℃~100℃ |
| Uniformity over the platform | ≦ ±0.3 ℃ |
| Temperature Calibration | Yes |
| Temperature stability | ± 0.5 ℃ |
| Display Accuracy | 0.1 ℃ |
| Shaking speed | 200-1500 rpm/min (increase: 1 RPM) |
| Orbit | 2 mm |
| Heating Time (from 20 ℃ to 100 ℃) | ~ 6 ℃ /min |
| Cooling time | ≤12min(from RT. to RT.-10 ℃) ≤15min(from 100 ℃ to RT.+10 ℃) |
| Operation mod | Constant operation: Constant temperature(RT+5~100℃) Timer: 0 ~ 99hrs 59min |
| Block Bath | Standard and customized types are available Four types of Standard block: A-block: 96 x 0.2ml B-block: 54 x 0.5ml C-block: 35 x 1.5ml D-block: 35 x 2.0ml |
| Unit Dimension | 212 x 300 x180 mm (W x L x H) |
| Weight | 5 kg |
| Rated Voltages | 110 / 220V |
| Power Supply | 220V /110V 2.5A 60/50HZ, Max. 150VA |

Block Type

| Cat. No. | Product Name | Descriptions | Max. Temp | Min Temp. | Max.Speed (rpm) |
| --- | --- | --- | --- | --- | --- |
| FATSM-A |  | 96×0.2ml | 100℃ | -10℃ | 1500 |
| FATSM-B |  | 54×0.5 ml | 100℃ | -10℃ | 1500 |
| FATSM-C |  | 35×1.5ml | 100℃ | -10℃ | 1500 |
| FATSM-D |  | 35×2.0ml | 100℃ | -10℃ | 1500 |
| FATSM-E |  | 15×0.5 ml+20×1.5ml | 100℃ | -10℃ | 1500 |
| FATSM-F |  | 24×Dia.≤φ12mm tube | 100℃ | 0℃ | 1200 |
| FATSM 02 |  | 12×15ml Falcon | 100℃ | 0℃ | 750 |
| FATSM 05 |  | 6×50ml Falcon | 100℃ | 0℃ | 750 |

Ordering Information

| Catalog # | Product Name | Block Capacity | Operating Temp. Range | Dimensions (L x W x H) |
| --- | --- | --- | --- | --- |
| FATSM 002 | Favor Thermo Shaker w/Cooling & Heating Function | 1 | -10℃~100℃ | 300mmx 212mm x 180mm |