Favor Gel Image Manager

Integrated type with Digital CCD Camera

Favorgen Gel Image Manager is the real time system for image viewing, capturing and printing DNA & Protein Gel after the electrophoresis experiment. Compact Darkroom design occupies minimum bench space. The easy access door allows easy placement and removal of even large gels. This is easy to use software for image capture, enhancement, annotation, storage and Printing. Users can use the digital camera to take the picture of the gel on the UV Transiluuminator and then input the picture into the computer.  The Gel image can be saved in file.

Features

1. The system is easy to use and produces publication of EtBr, SYBR green and Coomassie-stained gels.

2. 10x better resolution than over other systems means clearer, sharper bands.

3. Detection sensitivity under 30pg of ethidium bromide stained DNA.

4. Capture high quality digital images of trans-illumination from your UV or

white light box.

5. White light epi-illumination mode built in.

6. Integrated gel doc system.

7. The angle of monitor is adjustable.

8. USB saver to save the gel images.

Specifications

Camera

Sensor	Sony 1/2-inch Progressive Scan CCD

Color filter 	RGB Bayer

hutter control  	Electronic global shutter/progressive scan readout

Number of pixels  	1.4 M pixel

Max scaled resolution  	1,392 x 1,040

Sensitive area  	6.3mm x 5mm

Pixel size  	4.65um x 4.65um

Color depth  	12 Bit

Dynamic range  	>50 dB

Exposure time  	1ms ~ 60sec

Exposure control : 	Auto / Manual

Dark current : 0.15 e/pixel/sec

Quantum efficiency

Relative : Blue 475mm 74%, Green 540mm 95%, Red 620mm 91%

Live image  	On computer screen

Live image size 	Fit to windows

Shading correction  	Yes, stored for all formats

Cooling  	Peltier thermoelectric device cooling

Temperatures stability  	±1°C per 8-hr period

White balance 	Auto / Manual

Digitization : 	Pixel by digitization in camera head at CCD chip

Camera window : 	320 ~ 900nm

Pixel readout rate : 	12.24.32 Bit Live Image for R.G.B

UV/IR Interference Filter & Macro Zoom lens         1 PKG

IEEE1394 Interface Board & Interface Cable		 1 EA

Chamber

| Multi-power Source | 110/220V available |
| --- | --- |
| Inner White Lamp | Included inside |
| Safety Door Switch | Possible in Main Switch |
| Chamber Dimension | 510 x 390 x 340 mm (H x W x L) |
| Chamber construction Material | Metal/Steel |
| Chamber Weight | 15.0Kgs |
| Camera holder & Quick Shoe | Yes |
| View window for gel visualization | Yes |
| Epi-illumination | Yes |
| TFT Screen | Yes |

Screen

| Screen | TFT liquid crystal touch screen |
| --- | --- |
| Size | 7” |
| Resolution | 336960dot |
| Display mod | 16:9 |
| Video and Audio input | Dual available |

Bandpass Filter

| Bandwidth | 10+/-2nm |
| --- | --- |
| Center wavelength | 590nm |
| Size | 52mm diameter |
| Blocking | X-ray to FIR |
| Optical Density | 4 |

UV Transilluminator

| UV wavelength | 6 x 8W 312 nm |
| --- | --- |
| Big Filter Size | 200x200mm |
| Sensitivity | 100 - 70％ adjustable |
| Rated Voltages | 110 / 220V |
| Supply Power | 220V/60Hz |
| UV Safety Screen | Yes |
| UV intensity level | Convert freely 25% to 100% by using changeable-intensity control |

Filter  	200 x 200mm

Brightness	10000㎼cm2

Saver

| USB Saver | 1 EA |
| --- | --- |

Software

Analysis & Annotations 1-D Software                   1 copy

| Cat. No. | Product Name | Description |
| --- | --- | --- |
| FAGIM 003-DC | Gel Documentation & Analysis System: Favor Gel Image Manager-Integrated Type with Digital CCD Camera | Compact Digital Image System: Digital CCD Camera 1.4 M pixel 7''TFT color touch screen , Macro Zoom lens & UV/IR filter chamber, 312 nm UV transilluminator USB Saver Analysis & Annotations 1-D Software |

| Cat. No. | Product Name | Description |
| --- | --- | --- |
| FAAS 8000-402-1D | Analytic Software | 1-D Analytic Software |
| FAAS 9000-402-2D | Analytic Software | 2-D Analytic Software |